## Slide 1: Digital Design & Computer Arch. Lab 7 Supplement: Writing Assembly Code
Prof. Onur Mutlu
ETH Zurich
Spring 2020
23 March 2020

## Slide 2: Writing Assembly Code
In Lab 7, you will write MIPS Assembly code
You will use the MARS simulator to run your code
References
  H&H Chapter 6
  Lectures 9 and 10
    https://safari.ethz.ch/digitaltechnik/spring2020/doku.php?id=schedule
  MIPS Cheat Sheet
    https://safari.ethz.ch/digitaltechnik/spring2020/lib/exe/fetch.php?media=mips_reference_data.pdf

## Slide 3: An Example of MIPS Assembly Code
Add all the even numbers from to
int sum = 0;
for(int i = 0;i <= 10;i += 2) {
sum += i;
}
# i=$s0; sum=$s1
addi $s0, $0, 0
addi $s1, $0, 0
addi $t0, $0, 12
loop: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 2
j loop
done:
High-level code
MIPS assembly

## Slide 4: Recall: Arrays: Code Example
We first load the base address of the array into a register (e.g., $s0) using lui and ori
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# array base address = $s0
# Initialize $s0 to 0x12348000
lui $s0, 0x1234
ori $s0, $s0, 0x8000
lw $t1, 0($s0)
sll $t1, $t1, 1
sw $t1, 0($s0)
lw $t1, 4($s0)
sll $t1, $t1, 1
sw $t1, 4($s0)
High-level code
MIPS assembly
Notes: This slide belongs to Lecture 10

## Slide 5: Lab 7: Exercise 1
Write MIPS assembly code to compute the sum given two inputs and .
Example
  
For this exercise, you can use a subset of MIPS instructions: ADD, SUB, SLT, XOR, AND, OR and NOR, which are the instructions supported by the ALU you designed in the previous labs
Additionally, you are allowed to use J, ADDI and BEQ

## Slide 6: Lab 7: Exercise 2
Write MIPS assembly code to compute the Sum of Absolute Differences of two images
Hints
  Recall the function calls and the use of the stack in Lecture 10
  Read how to implement recursive function calls in H&H 6.4

## Slide 7: Last Words
In this lab, you will do what a compiler does: transforming high level code to MIPS assembly
Exercise 1: Write simple code and get familiar with the MARS simulator
Exercise 2: Sum of Absolute Differences of two images
Find Exercise 3 in the lab report

## Slide 8: Digital Design & Computer Arch. Lab 7 Supplement: Writing Assembly Code
Prof. Onur Mutlu
ETH Zurich
Spring 2020
23 March 2020

## Slide 9: Backup Slides

## Slide 10: MIPS R-Type Instructions
Description: | Add two registers and store the result in a register $d.
Operation: | $d = $s + $t; advance_pc (4);
Syntax: | add $d, $s, $t
Description: | Subtract $t from $s and store the result in $d.
Operation: | $d = $s - $t; advance_pc (4);
Syntax: | sub $d, $s, $t
Description: | If $s is less than $t, $d is set to one. $d gets zero otherwise.
Operation: | if $s < $t: $d = 1; advance_pc (4); else: $d = 0; advance_pc (4);
Syntax: | slt $d, $s, $t
Description: | Bitwise and of $s and $t and store the result in the register $d.
Operation: | $d = $s & $t; advance_pc (4);
Syntax: | and $d, $s, $t
Description: | Bitwise logic or of $s and $t and store the result in $d.
Operation: | $d = $s ¦ $t; advance_pc (4);
Syntax: | or $d, $s, $t
Description: | Exclusive or of $s and $t and store the result in $d.
Operation: | $d = $s ^ $t; advance_pc (4);
Syntax: | xor $d, $s, $t
ADD
SUB
SLT
XOR
AND
OR

## Slide 11: MIPS I-Type Instructions
Description: | Add sign-extended immediate to register $s and store the result in $t.
Semantics: | $t = $s + imm; PC=PC+4;
Syntax: | addi $t, $s, imm
Description: | Branch if the contents of $s and $t are equal.
Semantics: | if $s == $t: advance_pc (offset << 2)); else: PC=PC+4;
Syntax: | beq $s, $t, offset
ADDI
BEQ

## Slide 12: MIPS J-Type Instructions
Description: | Jump to the address.
Semantics: | PC = nPC; nPC = (PC & 0xf0000000) ¦ (target << 2);
Syntax: | j target
J